## Slide 1: Modeling machine failure in the IoT era
Danielle Dean, PhD
Senior Data Scientist Lead
Microsoft

## Slide 2: Outline
Predictive Maintenance Use Cases
Building E2E solution with Cortana Analytics Suite
Data
Modeling, Evaluation

## Slide 3: Predictive Maintenance Concepts
Important task in Internet of Things applications
Goal: improve production/maintenance efficiency
 | Predictive Maintenance in IoT | Traditional Predicative Maintenance
Goal | Improve production and/or maintenance efficiency | Ensure the reliability of machine operation
Data | Data stream (time varying features), Multiple data sources | Very limited time varying features
Scope | Component level, System level | Parts level
Approach | Data driven | Model driven
Tasks | Failure prediction, fault/failure detection & diagnosis, maintenance actions recommendation, etc. Essentially any task that improves production/maintenance efficiency | Failure prediction (prognosis), fault/failure detection & diagnosis (diagnosis)

## Slide 4: Predictive Maintenance Use Cases
Aerospace
Is the ATM going to dispense the next 5 notes without failing?
Utilities
When is this aircraft component likely to fail next?
Which circuit breakers in my system are likely to fail in the next month?
What is the root cause of the test failure?
Will the component pass the next stage of testing on factory floor or do I need to rework?
Should I replace the break disks in my car or can I wait for another month?
When is my solar panel or wind turbine going to fail next?
What is the likelihood of delay due to mechanical issues?
Manufacturing
Transportation & Logistics
What maintenance task should I perform on my elevator?

## Slide 5: Cortana Analytics Suite Transform data into intelligent action
Business Scenarios
Recommendations,
customer churn,
forecasting, etc.
Perceptual Intelligence
Face, vision
Speech, text
Personal Digital Assistant
Cortana
Dashboards and Visualizations
Power BI
Machine Learning and Analytics
Azure
Machine Learning
Azure
HDInsight (Hadoop)
Azure
Stream Analytics
DATA
Business apps
Custom apps
Sensors and devices
INTELLIGENCE
ACTION
People
Automated Systems
Big Data Stores
Azure
Data Lake
Azure
SQL Data Warehouse
Information Management
Azure
Data Factory
Azure
Data Catalog
Azure
Event Hub

## Slide 6: Today’s Talk
Business Scenarios
Maintenance scheduling, parts ordering…
Dashboards and Visualizations
Power BI
Machine Learning and Analytics
Azure
Machine Learning
Azure
Stream Analytics
DATA
Sensors and devices
INTELLIGENCE
ACTION
People
Automated Systems
Data Stores
Azure
SQL Database
Information Management
Azure
Data Factory
Azure
Event Hub

## Slide 7: Aircraft Engine Demo

## Slide 8: Scenario
This is Kyle.
Kyle manages a team that maintains aircrafts.
His job is to make sure that his 100 aircrafts are running properly & especially that the aircraft engines don’t need service.
Kyle wants to prevent delays due to mechanical issues so his customers will be happy.

## Slide 9: Scenario
Sadly, engines occasionally show signs of problems & must be taken out of service for maintenance or replacement.
To eliminate this occurrence, Kyle must maintain operations & figure out the best way to utilize resources in order to minimize delays due to mechanical issues.

## Slide 10: Questions & Solutions
3. Which engines are likely to fail in the future?
Cortana Analytics to the Rescue!
1. How long did engines run in the past?
2. Which are showing signs of failure?

## Slide 11: Components
Azure
Machine Learning Batch API
Azure
Stream Analytics
Azure
SQL Database
Azure
Data Factory
Training Data:
Aircraft engine run to failure data from NASA Ames Prognostics Data Repository
Aircraft engine real-time data based on NASA Ames Prognostics Data Repository
Azure
Blob Storage
1 4
2
3
Power BI
Real-time
Batch updates
Azure
Event Hub

## Slide 12
Sample training data
~20k rows,
100 unique engine id
Sample testing data
~13k rows,
100 unique engine id
Sample ground truth data
100 rows
Please refer to following link of doc for Data description section

## Slide 13: Conclusion
With the visualization prowess of Power BI, business owners can easily examine the performance of their entire company.
The Internet of Things and Stream Analytics connect data directly from the source to a dashboard to constantly track anomalies and asset performance in real-time.
Azure Machine Learning catches the problem before it becomes a problem. It streamlines operations without wasting resources.
Kyle is a happy man!

## Slide 14: Is the customer ready for ML?
Question is sharp.
Data measures what they care about.
Data is connected.
Data is accurate.
A lot of data.
The better the raw materials, the better the product.
E.g. Predict whether component X will fail in the next Y days
E.g. Identifiers at the level they are predicting
E.g. Will be difficult to predict failure accurately with few examples
E.g. Failures are really failures, human labels on root causes
E.g. Machine information linkable to usage information

## Slide 15: Qualification Criteria
For ML-based solution:
Problem is predictive in nature
Clear path of action if potential failures detected
Data with sufficient quality
  For predicting time left to failure, do you have failures or some proxy recorded?
  Do you have enough failures to be able to model?
  Is the “non-IoT” data in usable format?
  Can the domain knowledge, such as timing of maintenance recordings, be translated into usable data for modeling?

## Slide 16: Data Sources
The failure history of a machine or component within the machine.
The repair history of a machine, e.g. previous maintenance records, components replaced, maintenance activities performed. Maintenance types.
The operation conditions of a machine, e.g. data collected from sensors.
FAILURE HISTORY
REPAIR HISTORY
MACHINE CONDITIONS
The features of machine or components, e.g. production date, technical specifications.
Environmental features that may influence a machine’s performance, e.g. location, temperature, other interactions.
The attributes of the operator who uses the machine, e.g. driver.
MACHINE FEATURES
OPERATING CONDITIONS
OPERATOR ATTRIBUTES

## Slide 17: Feature Engineering
The process of creating features that provide better or additional predictive power to the learning algorithm.
a1 | a2 | … | a21 | sd1 | sd2 | … | sd21 | RUL | label1 | label2
40+ engineered features
  Other potential features: change from initial value, velocity of change, frequency count over a predefined threshold

## Slide 18: Example Feature Engineering Methods
2- Lag features for short term:
For each labelled record of an asset, pick a window of size w and use tumbling windows to create aggregate features for the periods before the labelling date and time.
3- Lag features for long term:
For each labelled record, find aggregated features for a larger window than w reflecting the long term effects.
Create features that capture degradation over time.
1- Rolling aggregates:
For each labelled record of an asset, pick a rolling window of size w, compute rolling aggregate features for the periods before the labelling date and time of that record.

## Slide 19: Modelling Techniques
Predict failures within a future period of time
BINARY CLASSIFICATION
Predict failures with their causes within a future time period.
Predict remaining useful life within ranges of future periods
MULTICLASS CLASSIFICATION
Predict remaining useful life, the amount of time before the next failure
REGRESSION
Identify change in normal trends to find anomalies
ANOMALY DETECTION

## Slide 20: Data Labeling
id | cycle | … | RUL | label1 | label2
1 | 1 |  | 191 | 0 | 0
1 | 2 |  | 190 | 0 | 0
1 | 3 |  | 189 | 0 | 0
1 | 4 |  | 188 | 0 | 0
… |  |  | … | … | …
1 | 160 |  | 32 | 0 | 0
1 | 161 |  | 31 | 0 | 0
1 | 162 |  | 30 | 1 | 1
1 | 163 |  | 29 | 1 | 1
1 | 164 |  | 28 | 1 | 1
1 | 165 |  | 27 | 1 | 1
1 | 166 |  | 26 | 1 | 1
1 | 167 |  | 25 | 1 | 1
1 | 168 |  | 24 | 1 | 1
1 | 169 |  | 23 | 1 | 1
1 | 170 |  | 22 | 1 | 1
1 | 171 |  | 21 | 1 | 1
1 | 172 |  | 20 | 1 | 1
1 | 173 |  | 19 | 1 | 1
1 | 174 |  | 18 | 1 | 1
1 | 175 |  | 17 | 1 | 1
1 | 176 |  | 16 | 1 | 1
1 | 177 |  | 15 | 1 | 2
1 | 178 |  | 14 | 1 | 2
1 | 179 |  | 13 | 1 | 2
1 | 180 |  | 12 | 1 | 2
1 | 181 |  | 11 | 1 | 2
1 | 182 |  | 10 | 1 | 2
1 | 183 |  | 9 | 1 | 2
1 | 184 |  | 8 | 1 | 2
1 | 185 |  | 7 | 1 | 2
1 | 186 |  | 6 | 1 | 2
1 | 187 |  | 5 | 1 | 2
1 | 188 |  | 4 | 1 | 2
1 | 189 |  | 3 | 1 | 2
1 | 190 |  | 2 | 1 | 2
1 | 191 |  | 1 | 1 | 2
1 | 192 |  | 0 | 1 | 2
Predefined window size for classification models
w1 = 30
w0 = 15
w1
w0
Regression
Binary classification
Multi-class classification

## Slide 21: ML Process
Define Objective
Access and Understand the data
Pre-processing
*
*Depending largely on size/complexity, may want to do pre-processing and/or feature/target construction before ingesting into AML Studio / AML API.
Historical Data
[features + labels]
Training Data
[features + labels]
Testing Data
[features + labels]
Future Data
[features only]
Split
Train Model
[model learns from training data]
Score Model
[model predicts on testing data]
Evaluate Model
[Compare predicted results and true labels]
Score Model
[model predicts on future data]
Prediction Results

## Slide 22
“Most IoT data are not used currently…
the data that are used today are mostly for anomaly detection and control, not optimization and prediction, which provide the greatest value.”1
Notes: Most IoT customer are looking for basic monitoring first (although they know there is value in ML). However, should think about ML and next steps because of importance of capturing data over long period of time! Most ML models need historical data to train.
-many customers we speak to need to re-do their data collection and come back at a later time after they start collecting the right data

## Slide 23
Learn from Cortana Analytics Gallery http://gallery.azureml.net (“predictive maintenance template” in collection)
Go Dos

## Slide 24: Acknowledgements
We utilized the following publically available data to help us generate realistic data for this pre-configured solution. We received assistance in creating this solution as a result of this repository and the donators of the data.
“A. Saxena and K. Goebel (2008). "PHM08 Challenge Data Set", NASA Ames Prognostics Data Repository (http://ti.arc.nasa.gov/project/prognostic-data-repository), NASA Ames Research Center, Moffett Field, CA.”
Quote on Slide 23: McKinskey Global Institute, The Internet of Things: Mapping the Value beyond the hype